## Slide 1: CHAMPSIM – BRANCH PREDICTOR
AUTHORS: Muhammad Ijaz, David Roche, Juš Osojnik
BARCELONA 2025

## Slide 2: INTRODUCTION
What is a branch predictor?
  Modern CPUs execute instructions out-of-order to improve performance.
  When a program encounters a branch (if/else, loop, function call), the CPU must guess the outcome to stay ahead.
  A branch predictor makes these guesses before the actual outcome is known.
  Accurate predictions reduce pipeline stalls and improve Instructions Per Cycle (IPC).
  Our goal: Implement a modern and accurate branch predictor using the TAGE algorithm.

## Slide 3: TAGE – BRANCH PREDICTOR
TAGE stands for Tagged GEometric history length predictor.
Key Components:
  Global History Register: Encodes taken/not-taken outcomes.
  Tagged Tables: Multiple tables indexed with varying history lengths.
  Tag Matching: Ensures predictions come from relevant context.
  Alternate Prediction Logic: Uses less confident tables if needed.
  Bimodal Table: Simple predictor used as a fallback.

## Slide 4: TAGE – HOW IT WORKS?
Instruction Pointer (IP) of the branch is received.
Global History Register is folded and combined with IP to:
  Compute index
  Compute tag
Search all tagged tables (longest history first) for matching tag.
  First match becomes the primary prediction.
  Second match (if any) is used as alternate prediction.
  Prediction strength is based on a 2-bit saturating counter, updated based on prediction correctness
If the confidence of the main match is low:
  Use the alternate match or fallback to bimodal prediction.
Final result → taken / not-taken.

## Slide 5: INITIAL RESULTS
Trace | IPC | Branch Prediction Accuracy | MPKI | Average ROB Occupancy at Mispredict
403.gcc-48B | 1.518 | 99.28 | 1.582 | 77.64
429.mcf-217B | 0.170 | 97.22 | 3.157 | 141.3
445.gobmk-30B | 1.132 | 84.43 | 29.28 | 13.67
456.hmmer-191B | 1.98 | 99.38 | 0.272 | 156.2
458.sjeng-283B | 1.276 | 91.22 | 19.88 | 24.81
600.perlbench_s-210B | 1.561 | 96.12 | 6.128 | 74.87

## Slide 6: TAGE - IMPROVEMENTS
Branch Type Awareness
Loop Bias Tracker
Useful Bit Aging
Confidence Tracking
Alternate Prediction Path
Global History Optimization
Prime-Spaced History Lengths
Return Address Stack (RAS)

## Slide 7: TAGE - IMPROVEMENTS
Branch Type Awareness
Detects branch category (e.g., direct jump, call, return, conditional).
Uses static predictions for easy-to-predict branches (e.g., direct jumps = taken).
Improves accuracy by avoiding unnecessary lookups for predictable branches.
Return Address Stack (RAS)
Specifically handles function return prediction.
On function call: push return address onto stack.
On return: pop address and compare to target.

## Slide 8: TAGE - IMPROVEMENTS
Confidence Tracking
Adds a confidence counter to each prediction entry.
Alternate Prediction Path
Keeps a backup prediction from a shorter-history table.
Tracks whether predictions are consistently accurate.
Helps decide whether to trust a weak prediction or defer to alternate.
Used when the primary (longest-history) prediction is weak or low-confidence.
Alt-selector counter learns when the alternate path is more trustworthy.

## Slide 9: TAGE - IMPROVEMENTS
Useful Bit Aging
Each TAGE entry has a “useful” bit to mark helpful entries.
Loop Bias Tracker
Tracks historical taken ratio of a conditional branch.
Periodically reset (aged out) to free up stale or unused entries.
Ensures tables don’t get filled with outdated predictors.
If a branch is taken 90%+ of the time, it's predicted as taken without TAGE logic.
Lightweight alternative to full loop-count prediction — less overhead.

## Slide 10: TAGE - IMPROVEMENTS
Prime-Spaced History Lengths
History lengths for each table use prime numbers (e.g., 5, 11, 17...).
Global History Optimization
Maintains a bitset of recent taken/not-taken outcomes.
Reduces aliasing and overlapping prediction behavior.
Gives diverse and independent views of past branches.
Crucial for indexing and hashing into tagged tables.
Can be tuned in length (e.g., 128 vs. 512 bits) to balance accuracy vs. storage.

## Slide 11: TAGE – PREDICTOR CONFIGURATION
Tagged Tables: 8
Entries per Table: 2048
Tag Bits per Entry: 12
Saturating Counter Bits: 3
Confidence Bits: 2
Valid & Useful Bits: 1 each
Global History Length: 512 bits
Bimodal Table Size: 2048 entries (3-bit counters)
Return Address Stack (RAS): 32-entry depth
Loop Bias Tracker: Tracks up to 512 IPs
Alt Selector Entries: 8 (one per table)

## Slide 12: RESULTS
Trace | IPC | IPC (new) | Branch Prediction Accuracy | Branch Prediction Accuracy (new) | MPKI | MPKI (new) | Average ROB Occupancy at Mispredict | Average ROB Occupancy at Mispredict (new)
403.gcc-48B | 1.518 | 1.499 | 99.28 | 99.15 | 1.582 | 1.854 | 77.64 | 77.64
429.mcf-217B | 0.170 | 0.171 | 97.22 | 98.11 | 3.157 | 2.152 | 141.3 | 141.3
445.gobmk-30B | 1.132 | 1.261 | 84.43 | 88.24 | 29.28 | 22.13 | 13.67 | 13.67
456.hmmer-191B | 1.98 | 1.981 | 99.38 | 99.45 | 0.272 | 0.2442 | 156.2 | 156.2
458.sjeng-283B | 1.276 | 1.321 | 91.22 | 92.16 | 19.88 | 17.76 | 24.81 | 24.81
600.perlbench_s-210B | 1.561 | 1.6 | 96.12 | 96.79 | 6.128 | 5.075 | 74.87 | 74.87

## Slide 13: CONCLUSION
Consistently Accurate Predictions: The predictor performed reliably across diverse workloads, showing strong accuracy and low misprediction rates.
Balanced Performance and Efficiency: Maintained solid IPC and minimized pipeline disruptions without excessive complexity.
Storage-Efficient Design: Achieved meaningful improvements using a compact and hardware-friendly configuration.

## Slide 14
Thank you for your atention